Annex No. 1: 	 Technical Conditions

Statement of accomplishment of the technical requirements

Part 1 - Quanterra Q330S+

Seismic digitizer and data logger  Quanterra Q330S+: 6 pieces, included five pieces of 3 channel loggers  and one piece of 6 channel logger

- Specification of device:

Quanterra Q330S+

- Device is up to following technical requirements::

| Minimal technical requirement: | Requirement fulfilled YES / NO. * |
| --- | --- |
| 24bit A/D converter |  |
| Input range 40V P-P at gain 1 |  |
| Input gain per channel: 1, 32 |  |
| Input filters linear or minimum phase FIR |  |
| Sample rate 1000 – 1Hz |  |
| Time base – precision TCXO locked to GPS |  |
| Full duplex, low latency telemetry over serial and Ethernet |  |
| Temperature range fully specified -20 to +50C |  |
| Sensor calibration signal step, sine, random |  |
| Extended SOH sets of channels |  |
| Internal RAM memory for seismic data 64MB |  |
| Ethernet interface 10/100BT, full IP protocol stack |  |
| Console port with serial interface |  |
| Dual internal USB data recorder, USB memory stick 64GB |  |
| Real-time data telemetry up to 3 independent central sites and internal USB recording system Dimensions 500 x 120 x 250mm maximum |  |
| Average power consumption 0,75W for 3 channels |  |
| Input impedance > 100 kohm, gain 1 |  |
| Input impedance > 1000 kohm, gain 32 |  |
| Active GPS antenna |  |
| Web interface for configuration and control of the seismic system and the data recorder |  |
| SSH server for remote data retrieval from data recorder |  |
| Software for configuration and control of the seismic system and the data recorder |  |
| Software for data recording |  |
| Software for viewing of recorded data |  |
| Sensor pigtail cable: 3 chanell data logger – 5 pieces 6 chanell data logger – piece |  |

* Supplier shell fill YES / NO

Corporate name of Supplier:

Person entitled to act on behalf of Supplier:

Address of Contractor

Date:

Signature:

Part 2 - Passive 3D seismometer Sercel  L4C-3D

7 pieces of  Passive 3D seismometers Sercel  L4C-3D

- Specification of device:

Sercel L4C-3D

- Device is up to following technical requirements:

| Minimal technical requirement | Requirement fulfilled YES / NO* |
| --- | --- |
| Natural frequency 1Hz ( +/- 0,1Hz ) |  |
| Three directional seismometer |  |
| Minimum sensitivity 270 V/m/s |  |
| Coil resistance < 6000 ohm |  |
| Shunt resistor value < 15 000 ohm |  |
| Humbuck construction of signal coils |  |
| Coil travel Pk-Pk > 6mm |  |
| Calibration coil |  |
| Operating temperature -20 to 50°C |  |
| Waterproof case |  |
| Sensor pigtail cable cablel 50 ft … 5 pieces cable 10 ft … 2 pieces |  |

* Supplier shall fill YES / NO

Corporate name of Supplier:

Person entitled to act on behalf of Supplier:

Address of Contractor

Date:

Signature: