Technical Specifications

All the seismic instrumentation equipments are ment for a modernization of the existing local seismic networks MONET and CRSN.

Part 1 - Seismic data logger (2 pieces)

Device meets following minimal requirements

| Producer |  |
| --- | --- |
| Type/Manufacturing code |  |

| Minimal technical requirement: | Requirement fulfilled YES / NO or tech. specifications offered by supplier |
| --- | --- |
| 3 channel data input |  |
| 24bit A/D converter |  |
| Input range 40V P-P at gain 1 |  |
| Input gain per channel: adjustable 1 and 32 |  |
| Composite input filters linear or minimum phase FIR |  |
| Sampling rate 1000 – 1Hz |  |
| Time base – precision TCXO locked to GPS |  |
| Data transmission full duplex, low latency telemetry over serial and Ethernet |  |
| Min guaranteed operating temperature -20°C to +50°C |  |
| Sensor calibration signal generation step, sine, random |  |
| Extended SOH channels (e.g., temperature, DC voltage and GPS status) |  |
| RAM memory for seismic data 60MB |  |
| Ethernet interface 10/100BT, full IP protocol stack |  |
| Console port with serial interface |  |
| Dual data storage, 2x USB memory stick 60GB |  |
| Real-time data telemetry to up to 3 independent central sites and internal USB storage system |  |
| Dimensions 500 x 120 x 250mm maximum |  |
| Average power consumption <1W for 3 channels |  |
| Input impedance > 100 kohm, gain 1 |  |
| Input impedance > 1000 kohm, gain 32 |  |
| Active GPS antenna |  |
| Web interface for configuration and control of the seismic system and the data storage |  |
| SSH server for remote data retrieval from data storage |  |
| Software for configuration and control of the seismic system and the data storage |  |
| Software for data recording |  |
| Software for viewing of stored data |  |
| Sensor pigtail cable – 1 piece for one of the two dataloggers only |  |

Part 2: Seismometer - type 1; 1 piece

Device meets following minimal requirements

| Producer |  |
| --- | --- |
| Type/Manufacturing code |  |

| Minimal technical requirement | Requirement fulfilled YES / NO or tech. specifications offered by supplier |
| --- | --- |
| Three directional seismometer (velocity sensor) |  |
| Natural frequency 1Hz |  |
| Minimum sensitivity 700 V/m/s, differential outputs |  |
| Frequency band (-3 dB points): 1-100 Hz |  |
| Damping: 0.7– critical |  |
| Power supply 10-16 V DC |  |
| Typical power consumption: < 0.2 W |  |
| Dynamic range > 135 dB |  |
| RMS noise for 1 Hz: < 3 nm/s |  |
| Weight < 2 kg |  |
| Min guaranteed operating temperature -15°C to +50°C |  |
| Sensor cable 2 m with Reftek connector |  |

Part 3: Seismometer - type 2; 1 piece

Device meets following minimal requirements

| Producer |  |
| --- | --- |
| Type/Manufacturing code |  |

| Minimal technical requirement | Requirement fulfilled YES / NO or tech. specifications offered by supplier |
| --- | --- |
| Three directional seismometer |  |
| Frequency band (-3 dB points): 5 s - 50 Hz |  |
| Minimum sensitivity 700 V/m/s, differential outputs |  |
| Damping 0.7 - critical |  |
| Power supply 10-16 V DC |  |
| RMS noise at 1 Hz: < 1 nm/s |  |
| Dynamic range > 135 dB |  |
| Typical power consumption < 0.2 W |  |
| Output voltage range 40 V peak to peak |  |
| Min guaranteed operating temperature -15°C to +50°C |  |
| Sensor cable 5 m to Quanterra dataloggers |  |

Part 4: Seismometer - type 3; 1 piece

Device meets following minimal requirements

| Producer |  |
| --- | --- |
| Type/Manufacturing code |  |

| Minimal technical requirement | Requirement fulfilled YES / NO or tech. specifications offered by supplier |
| --- | --- |
| Three directional seismometer |  |
| Frequency band (-3 dB points): 40 s - 100 Hz |  |
| Minimum sensitivity 700 V/m/s, differential outputs |  |
| Damping 0.7 - critical |  |
| Calibration input |  |
| Power supply 10-16 V DC |  |
| Typical power consumption < 0.5 W |  |
| Output voltage range 40 V peak to peak |  |
| Min guaranteed operating temperature -30°C to +50°C |  |
| Sensor cable 10 m to Quanterra dataloggers |  |