Technické podmínky

Technické podmínky jsou vyhotoveny jak v českém, tak anglickém jazyce. V případě rozporů mezi českou 
a anglickou jazykovou verzí, nebo v případě sporu o výklad použitých pojmů, má přednost česká jazyková verze.

Kryogenní systém s uzavřeným cyklem

Popis zařízení a jeho využití

Héliový chladicí systém s uzavřeným cyklem, který je určen pro připojení průtokových héliových kryostatů. Zařízení umožňuje dosažení velmi nízkých teplot pro fyzikální experimenty bez potřeby kapalného hélia. Zároveň je možné recyklovat odpařené hélium a značně tím snížit spotřebu velmi drahého hélia a šetřit provozní náklady. V první fázi předpokládáme použití zejména pro rentgenovou strukturní analýzu za nízkých teplot, kdy bude použit stávající průtokový kryostat v majetku zadavatele. Budou tím studovány zejména strukturní fázové přechody spojené se změnami elektronové struktury nebo magnetického uspořádání.

Chladicí systém se skládá z héliového chladicího kompresoru, chladicího systému a oběhového kompresoru, který zajišťuje oběh chladicí kapaliny připojeným héliovým průtokovým kryostatem. Odpařené hélium je sbíráno systémem a znovu použito v chladicím systému. Součástí jsou rovněž nezbytná propojení jednotlivých částí 
a hlavice pro připojení k průtokovému kryostatu. Zařízení bude možné použít i s jinými průtokovými héliovými kryostaty.

Předmětem dodávky je kompletní, nové, nepoužité a zcela funkční zařízení.

| Parametr | Parametr nabízený dodavatelem |
| --- | --- |
| Výrobce |  |
| Typ/Model |  |

| Minimální požadované technické parametry | Technické parametry nabízené dodavatelem* |
| --- | --- |
| Uzavřený cyklus chladicího hélia | (Dodavatel uvede ANO/ NE) |
| Vodou chlazený héliový kompresor | (Dodavatel uvede ANO/ NE) |
| Kompatibilita s průtokovým kryostatem ColdEdge výr.č. 091718. Připojovací trubice kompatibilní se systémem Stinger / Cooltran | (Dodavatel uvede ANO/ NE) |
| Chladicí výkon pro připojený kryostat alespoň 0.4 W při teplotě 4.2 K | (Dodavatel uvede ANO/ NE a skutečnou hodnotu) |
| Délka připojovací trubice ke kryostatu min 1,5 m | (Dodavatel uvede ANO/ NE a skutečnou hodnotu) |
| Zařízení pro připojení do sítě 240V/50Hz (jedna fáze) a 400V/50Hz (tři fáze) | (Dodavatel uvede ANO/ NE) |

*Dodavatel uvede ANO/NE a doplní požadované informace. Pokud dodavatel doplní do Minimálních požadovaných technických parametrů NE, je to důvod pro vyloučení uchazeče z další účasti v zadávacím řízení. Dodavatel je povinen přiložit k této technické specifikaci i svou vlastní technickou specifikaci či svůj vlastní popis zařízení.

The technical conditions

The technical conditions are in both Czech and English. In the event of a discrepancy between the Czech and English language versions, or in the event of a dispute as to the interpretation of the terms used, the Czech language version shall prevail.

Closed-cycle cryogenic system

Equipment description and its use

Closed-cycle helium refrigeration system designed to connect flow-through helium cryostats. The device allows very low temperatures to be achieved for physical experiments without the need for liquid helium. At the same time, it is possible to recycle the evaporated helium, thus significantly reducing the consumption of very expensive helium and saving operating costs. In the first phase, we foresee the use mainly for low-temperature X-ray structural analysis using an existing flow cryostat owned by the customer. In particular, structural phase transitions associated with changes in electronic structure or magnetic ordering will be studied.

The cooling system consists of a helium refrigeration compressor, a refrigeration system and a circulating compressor which circulates the coolant through the connected helium flow cryostat. Evaporated helium is collected by the system and reused in the cooling system. Also included are the necessary interconnections between the individual parts and the head for connection to the flow cryostat. The equipment will also be usable with other helium flow cryostats.

The delivery includes complete, new, unused and fully functional equipment.

| Parameter | Parameter offered by supplier |
| --- | --- |
| Producer |  |
| Typ/Model |  |

| Minimal required technical parameters | Technical parameters offered by the supplier* |
| --- | --- |
| Closed-cycle helium refrigeration | (Supplier shall indicate YES/ NO) |
| Water cooled helium compressor | (Supplier shall indicate YES/ NO) |
| Compatibility with ColdEdge flow cryostat part no. 091718. Connection tube compatible with Stinger / Cooltran system | (Supplier shall indicate YES/ NO) |
| Cooling capacity for connected cryostat at least 0.4 W at 4.2 K | (Supplier shall indicate YES/ NO and actual value) |
| Length of connecting tube to cryostat min 1.5 m | (Supplier shall indicate YES/ NO and actual value) |
| 240V/50Hz mains connection (single phase) and 400V/50Hz (three phases) | (Supplier shall indicate YES/ NO) |

*The supplier shall indicate YES/NO and complete the required information. If the Supplier adds NO to the Minimum Required Technical Parameters, this shall be grounds for disqualification of the Bidder from further participation 
in the procurement process. The Supplier shall be required to attach its own technical specification or its own description of the equipment to this Technical Specification.