Technical Specifications

PURPOSE AND SUBJECT OF THE PUBLIC CONTRACT

The purpose of the delivery is to obtain a system for operant IV self-administration.

The subject of delivery is new and fully functional equipment including complete installation, commissioning and training of personnel at the delivery site.

The bidder's bid must meet all the requirements and parameters specified by the Contracting Authority below. In the case of parameters defined by a minimum or maximum level or range of values, the tenderer's tender must meet at least the specified required level.

MINIMUM TECHNICAL PARAMETERS

| Parameter | Parameter offered by the supplier |
| --- | --- |
| Producer | (Supplier to specify manufacturer) |
| Type/Model | (Supplier to specify type and model) |

| Minimum required technical parameters | Technical parameters offered by the supplier* |
| --- | --- |
| 16 operant chambers | Supplier shall specify YES/ NO |
| Laptop to control the system. 15 inch diagonal. | Supplier shall specify YES/ NO |
| Data acquisition software for 1 Laptop | Supplier shall specify YES/ NO |
| SW for data analysis, unlimited license | Supplier shall specify YES/ NO Supplier shall specify YES/ NO |
| Starter pack of system compatible consumables | Supplier shall specify YES/ NO |

| Specification of operant chambers (pcs per chamber) |
| --- |
| 1 sound-attenuating cubicle | Supplier shall specify YES/ NO |
| 1 fan (minimum) | Supplier shall specify YES/ NO |
| 3 retractable levers | Supplier shall specify YES/ NO |
| 3 nose-poke operands | Supplier shall specify YES/ NO |
| 3 stimulus lights (white) | Supplier shall specify YES/ NO |
| Tone generator, minimum 1 fixed tone generator | Supplier shall specify YES/ NO |
| IR beams for tracking of locomotor activity during session | Supplier shall specify YES/ NO Supplier shall specify YES/ NO |
| 2 house lights | Supplier shall specify YES/ NO |
| 1 pellet dispenser | Supplier shall specify YES/ NO |
| 1 reward tray with head entry detector | Supplier shall specify YES/ NO |
| 2 floors | Supplier shall specify YES/ NO |
| 2 waste pans | Supplier shall specify YES/ NO |
| 1 infusion pump with fixed speed (allowing 0.1 mL/5 seconds from 10 ml syringe) | Supplier shall specify YES/ NO |
| 2 one-channel stainless steel swivels | Supplier shall specify YES/ NO |
| 1 drug delivery arm | Supplier shall specify YES/ NO |

| General requirements |
| --- |
| System for stacking cubicles in two layers, with wheels | Supplier shall specify YES/ NO |
| System for safe and easy installation of the infusion pumps (e.g. internal or other shelf) | Supplier shall specify YES/ NO |
| All necessary hardware and cables for connecting the system with a limited number of required plugs (pre-wired) | Supplier shall specify YES/ NO |
| Plan for sterilization of the entire system when installed in the SPF user device | Supplier shall specify YES/ NO |

* The supplier shall indicate YES/NO and complete the required information.

The Supplier is obliged to attach his own technical specification or his own description of the equipment to the technical specification given in this table.